## Slide 1: White Point Landslipe Palos Verdes, CA
By Christian Kesler, Savannah Keane, and Sarva Pulla

## Slide 2: Site information
Palos Verdes, CA
On a bluff overlooking the Pacific Ocean
Roadway along top of the bluff

## Slide 3: Before failure - 2011

## Slide 4: After failure - 2013

## Slide 5: After failure - 2014

## Slide 6: After failure - 2015

## Slide 7: Utexas analysis before failure
Setup the location
Found distances and slope from Google Earth
Distributed load for the roadway

## Slide 8: Utexas analysis before failure

## Slide 9: Utexas pre-emptive solution
7 Reinforcement Lines
108 feet in length
Total cost is approximately $453,000

## Slide 10: UTExas pre-emptive solution

## Slide 11: results
Actual failure OF SLOPE
FS = 1.371
COST TO FIX = $32,000,000
pre-emptive failure with reinforcements
FS = 1.465
COST TO PREVENT = $453,000

## Slide 12: CURRENT CONDITIONS
Currently the road is blocked off on both sides of the slide
Construction to begin in 2019
Expected construction time is 2 years

## Slide 13: Recommendations
Dewatering on the eastern flank
Slope anchoring using post-tensioned tieback anchors
Reinforced Soil Slope (Granular Fill with steel or geosynthetic reinforcement)
Retaining Wall
Bridge
Regrading

## Slide 14: Potential costs
Immediate Measures (install monitoring points and drains, grade surface, and add slope anchors and traffic improvements) – $9.14 million. Option 1: Abandon Roadway – $0 Option 2: Restore road without a retaining wall – $43.8 million Option 3: Restore road with a retaining wall – $28.8 million Option 4: Restore road with a bridge – $51.3 million Option 5: Regrade road – $6.7 million Option 6: Reroute road – $6.9 million

## Slide 15: END
References
http://eng.lacity.org/whitepoint/White%20Point%20Final%20Main%20Body.pdf
http://www.geotechdata.info/parameter/angle-of-friction.html
http://www.geotechdata.info/parameter/cohesion.html
http://www.geotechnicalinfo.com/soil_unit_weight.html